COORDINATED SIGNAL TIMING

Coordination of traffic signals involves timing signals for opposing traffic streams with relation to one another, so that vehicles traveling at predetermined speeds will be able to successfully clear successive intersections on “green.”

In order to coordinate signals for opposing traffic streams, we use space-time diagrams.

Definitions:

Through band – space-time path intersecting green at successive signals.

Band width – width of total through band.

Offset- time difference between beginnings of green at two signals.

Time

Figure 1.  Space-Time Diagram

We will be considering only simple situations, where signal coordination can be determined by graphical methods, and calculations derived from the graph.

Example 1 – Design and Evaluation

Given:

Two intersections spaced 1400 ft. apart

Design speed of progression = 40 ft/sec

60 second cycle with 50-50 splits

a. Find the offsets required for progression in the direction A to B.

b. Assuming AB is a two-way street, find the bandwidth in the opposite direction.

Figure 2.  Analysis

Figure 3.  Evaluation

Steps:

Draw ideal band; Find loss; Find and draw total through band

Figure 4.  Final Product

Example 2 – Evaluation of Existing Operation

Given:

Intersection spacing shown in Figure 5.

Design speed = 40 ft/sec

60 second cycle with 50-50 splits

Half cycle offset at intersection B

Quarter cycle offset at intersection C

Figure 5.  Block Spacing.

Figure 6.  Show Ideal band, where edges hit red, calculate arrival times and signal changes.

Figure 7.  Draw the Total Through Band.

Figure 8.  Find Ideal Band for Opposite Direction.

Figure 9.  Draw Total Through Band.

Figure 10.  Final Diagram.

Signal Coordination Summary

- For this course, you must have a common cycle length for each intersection in your system.

- Identify the reference intersection, and determine all offsets with respect to it.

- Offsets must be an increment between zero and the cycle length.

- Progression band MUST go through entire system.

- You must determine a bandwidth for each direction of traffic progression.

- Good operation is achieved with bandwidth efficiencies of 40% or greater.

- Cycle lengths and splits should be calculated so that all traffic is passed at each intersection.

- It is typically not possible to have full progression in both directions.

- Available software:

  - Passer II

  - TRANSYT 7F

# Text boxes

Offset

Band width

C

B

A

Distance

Time (sec.)

120

90

65

60

Bandwidth

35

30

Offset of B

(relative to A)

5

1400’

B

A

Space (ft.)

5

95

65

35

1400’

Space (ft.)

30

60

120

Time (sec.)

90

Bandwidth

Bandwidth

Reduction of Band (10 sec.)

A

B

30

60

120

65

Time (sec.)

35

90

1400’

Space (ft.)

5

A

B

A

B

C

1330 ft.

1470 ft.

C

B

A

135

105

60

120

Time (sec.)

90

30

75

45

15

Offset B

Offset C

135

105

60

120

Time (sec.)

90

30

75

3.25 sec. loss

45

BW = 21.75 sec.

5 sec. loss

15

Offset C

Offset B

B

A

C

75

135

105

45

BW = 21.75 sec.

15

30

60

120

Time (sec.)

90

Offset C

Offset B

B

A

C

135

BW = 5 sec.

105

75

45

15

Offset C

BW = 21.75 sec.

30

60

120

Time (sec.)

90

Offset B

A

C

B

135

105

BW = 5 sec.

75

30

60

120

Time (sec.)

90

Offset C

Offset B

45

BW = 21.75 sec.

15

C

B

A